Manual for AutoRnLog
by Alessandro Capuana

Prerequisites:
To run the AutoRnLog.jar, a Java Runtime Environment (JRE) needs to be installed. AutoRnLog requires at least version 8 which can be downloaded here:

https://java.com/de/download/

An radlog.ini file needs to be provided in the directory of AutoRnLog.jar. Plese be sure to change the Name of the monitor you want to connect to and his IP in this *.ini file. For example:
IP=129.206.22.122
id=1_Heidelberg
Settings:
Follwing Settings should be changed according to the requirements in the *.ini file:

LowerFlagThres and UpperFlagThres change how much the edge of the spectrum can be shiftet against the Edgeoffset if you want them to get flagged (therefor not inside the Extract /Activity).
amount sets how many spectra should be pulled from the monitor. To get the right name of the spectra to be copied, the monitor time should be equal to the System time where AutoRnLog is operating.
evaluate sets how many spectra from lvl1 should be takes to calculate the Extract and Activity files.
Lvl0 and lvl1 is the path of the appropriate directories. Lvl0 should contain raw data, lvl1 the calculated data from AuroRnLog. Be sure to end the path with an “\” and not to use spaces.

Running AutoRnLog:
The program will try to connect to the monitor and get the specified amount of last spectra from the monitor. They will be safed into the lvl0 and lvl1 directories. The spectra from the lvl1 directory will then be browsed, using a temporary reference spectrum, and the extract.txt and activity.act files will be calculated into the lvl1 directory.

Change sourcecode:
AutoRnLog was written via Eclipse using the WindowBuilder extension. It can be downloaded here:
https://www.eclipse.org/windowbuilder/